## Slide 1
Intro
to
Flexibowl®
Solutions
and
Applications
ars Industrial Robotics and X-Ray

## Slide 2
Contents
FlexiBowl® and Options
Bulk Feeders and Motorised Hoppers
Market Benchmarking
Our Services
FlexiVision
Market Information and Reference

## Slide 3
FlexiBowl®: How it works
Motorised Hopper - Large parts storage capacity
Vibrating Bulk Feeder - Drops parts accurately
Wiper - Diverts parts from outer wall, back under picking area
Servo Driver - ethernet/UDP or digital I/O communication
Direct Drive Motor
Flip unit - turns and spreads parts
Blow Unit, Diverts tiniest parts from outer wall
Quick-change disc, Different colours, textures and coatings
Backlight, Red, White and Infrared colours
Toplight, Red, White and Infrared colours
FlexiVision, fully integrated vision system
Vision system controls FlexiBowl® movements, parts flow from the bulk feeder and sends coordinates to the robot
Parts are sorted by combined actuation of servomotor and flip unit
Acceleration, speed, flipping frequency and power parameters are set according to part geometry, material and dimension
0
1
2
3
4
5
6
7
8
9
10
ars Industrial Robotics and X-Ray

## Slide 4
Options: How they work
Backlight/ Toplight
Wiper
Rotary Disc
Blow Unit
Click on the picture to open the video
ars Industrial Robotics and X-Ray

## Slide 5
FlexiBowl® 500
FlexiBowl® 800
FlexiBowl® 650
Maximum part weight
Bulk storage capacity
Maximum pick widow
Pick widow (area)
Permissible load
Pick level above surface
Feeder weight
Recommended part size
FlexiBowl®: How to choose
5>x<50mm
<100gr
10/20dm3
205/360mm
475cm2
5kg
240mm
36kg
20>x<110mm
<170gr
20/40dm3
390/250mm
900cm2
5kg
270mm
51kg
60>x<250mm
<250gr
20/40dm3
390/315mm
1183cm2
5kg
270mm
71kg
1>x<15mm
<40gr
5/10dm3
125/220mm
177cm2
3kg
240mm
25kg
FlexiBowl® 350
ars Industrial Robotics and X-Ray

## Slide 6
Contents
FlexiBowl® and Options
Bulk Feeders and Motorised Hoppers
Market References
Our Services
FlexiVision
Market Information and References

## Slide 7
5, 10, 20 & 40 liters available for parts storage
Polyurethane coating is available as an option to reduce loud noise when handling metal components
Up to 300 liters avialble for parts storage
The hoppers are custom made and samples may be nedeed to define the set up
Options: Bulk storage
Vibrating bulk feeders
Motorized hoppers
Accurate and continuous parts flow
Large amount of parts can be stored
Combine them to get parts flow control with higher storage capacity
ars Industrial Robotics and X-Ray

## Slide 8
Contents
FlexiBowl® and Options
Bulk Feeders and Motorised Hoppers
Market Benchmarking
Our Services
FlexiVision
Market Information and References

## Slide 9
FlexiVision is an integrated PC-based vision software for robot guidance, developed on HALCON libraries.
It is designed for fast setup and deployment of FlexiBowl® applications.
FlexiVision: Vision system
FlexiVision user friendly interface
Control FlexiBowl® parameters
Calibrate the camera and the robot
Connect up to 3 cameras and 2 robot with a single dongle key
Design and manage your recipes
Geometry and pattern matching
Hundreds of industrial GigE cameras supported

## Slide 10
Robot Integrated Worldwide

## Slide 11
Contents
FlexiBowl® and Options
Bulk Feeders and Motorised Hoppers
Market Benchmarking
Our Services
FlexiVision
Market Information and References

## Slide 12
Typical Applications
FASHION ACCESSORIES
and PRECISION PARTS
Buckle, eyewear, knob, hinge..
MEDICAL DISPOSABLES
Stopcock, drip chamber,
syringe, needle, filter..
HOUSE APPLIANCES
PARTS
Oven, washing machine..
TOYS and GADGETS
Assembly, kits, pad printing
painting, packing..
HOUSE AND
PRSONAL CARE
Dispenser, spray pump,
toothbrush..
ELECTRICAL PARTS
Relay, connector, diode,
switch, coil..
AUTOMOTIVE PARTS
Mechanism, connection,
transmission,
fluid management..
COSMETICS
Lipstick, lids, brushes,
bottle, tube, cup..
CONSUMER
ELECTRONICS
Laptop, smartphone..
ars Industrial Robotics and X-Ray
MACHINE TENDING
CNC, welding, pad printing laser
marking, plastic moulding..

## Slide 13
Worldwide References: End Users
ars Industrial Robotics and X-Ray

## Slide 14
Contents
FlexiBowl® and Options
Bulk Feeders and Motorised Hoppers
Market Benchmarking
Our Services
FlexiVision
Market Information and References

## Slide 15
FlexiBowl®: Parameters
Easy to set up
ars Industrial Robotics and X-Ray

## Slide 16
Contents
FlexiBowl® and Options
Bulk Feeders and Motorised Hoppers
Market Benchmarking
Our Services
FlexiVision
Market Information and References

## Slide 17
Tech advisory
& support
Preliminary analysis
Viability tests
Feed rate optimization
Equipments
design
Training
System
ramp up
After-sale service
Remote
support
ARS leads all the way through
ars Industrial Robotics and X-Ray

## Slide 18
THANK YOU
Via Piero Gobetti, 19 | 52100 Arezzo (IT) Italy
Tel. +39 0575 398612 | Fax +39 0575 398620 | info@arsautomation.com
www.arsautomation.com | www.flexibowl.com
ARS Automation